## Slide 1: Universal Plastic Shredder V2.0
Team: I’m so Shredded Inc.
Bao Nguyen · Fearghus Tyler · Yaqoub Rabiah · Fox Kang

## Slide 2: Project Objectives(Electrical Only)
Drive an electric motor to power a plastic shredder
Ensure safe operation with buttons and/or HMI display
Design and wire the system to industry standards
  NEMA compliant electrical system
  NFPA 70 installation guidelines
$1000 Budget for EE team
  Consumer electronics, but with an extra zero

## Slide 3: Group Objectives(if budget and time allows)
Display and clear errors or lockouts on an HMI
Popup warning messages for faults and unsafe conditions
Telemetry data display
  Motor speed (RPM)
  Temperature
  Amps/Volts/Watts
  System status
    Auto unjam/retry
Capacitive Touch Safety Interlock(CTSI)
Why add all this complexity?
  4 EE team members + 6 months

## Slide 4: Circuit Overview(WIP)

## Slide 5: Safety Logic

## Slide 6: PLC Modules(DL205+H2-DM1E+Modules)
Ebay 350 used PLC rack+cpu+Modules
  H2-DM1E- CPU
  D2-08ND3- 8ch Digital input module
  F2-04RTD - Analog Temp module
  F2-08AD-1 -8ch Analog input module
  D2-08TD2 - 8ch Digital output module
  F2-02DA-1 -2ch Output module
Comes with analog I/O and Digital I/O
  Analog: Control VFD RPM
  Digital: Button/sensor inputs, control contactor output
Very expandable(for additional sensors)
  Up to 8 switches
Program
  Do-more designer

## Slide 7: HMI (AutomationDirect EA1-T4CL)
120-130 used
C-more programming software
  Simple, tag based programming
  Matching IDs to the PLC
RS-232 protocol
24VDC power
Touchscreen + Buttons

## Slide 8: VFD(AT5‑1500X)(We dont use this
$108
Single phase 115V in to 230V 3 Phase out
Two analog outputs
  For getting RPM, Current, Watts, Volts, Temp, etc
One analog input
  RPM Control
Has Modbus
  Allow for more than two telemetry
  Not limited by the analogo
Allows for the use of better 3-phase motors
  More efficient than 1-phase and Brushed motors
  Better throttle control

## Slide 9: Motor
Craigslist ad, listed at $100, 3HP 230V 1750 RPM (Powered by a VFD with an inverter 115/230V single phase to 3 phase at 3HP)

## Slide 10: BOM
Best Estimate So Far:

## Slide 11: Questions/Suggestions/Concerns